## Slide 1: XMC4500 USB Host Mass Storage Example
Getting Started V1.0

## Slide 2: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 3: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 4: Overview
This example demonstrates the implementation of USB host mass storage functionality. It is based on the free LUFA USB host stack implementation which is ported to XMC4500 family and provided within this example.
Within this documentation you will be guided through all the building blocks of a typical USB host mass storage application on the XMC4500 family. You will be able to connect a USB flash drive device supporting the FAT file system to the host and perform file read and write access to the device.
As a result you will be enabled to implement your own USB host mass storage functionality on the XMC4500 family.

## Slide 5: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 6: Requirements - hardware
XMC4500 General Purpose board CPU_45A-V3
USB cable micro-A plug to standard-A receptacle for host example
USB cable micro-B plug to standard-A plug for debugging
USB flash drive
Std-A receptacle
Micro-A plug
Flash Drive
Std-A plug
Micro-B plug

## Slide 7: Requirements – hardware & software
Windows laptop
DAVETM installed
7
July 2016
Copyright © Infineon Technologies AG 2016. All rights reserved.
DAVETM (v4.1.4 or Higher)
Download DAVETM free of charge
  Link : DAVETM v4 Download

## Slide 8: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 9: Setup - hardware
Flash Drive
Std-A receptacle
Micro-A plug
Micro-B plug
Std-A plug
Ensure proper cable types
Connect cables to the correct ports
Windows laptop running DAVETM

## Slide 10: Setup – import example project in to DAVETM
1

## Slide 11: Setup – import example project in to DAVETM
2
3

## Slide 12: Setup – import example project in to DAVETM
Check the folder structure of the imported project.
3
2
1
5
4
1
Free FAT file system code
2
Free LUFA USB stack, mass storage class and glue layer for XMC low level driver
3
Code linking FAT file system and USB mass storage layer
4
XMCLib folder contains USB low level driver in file xmc_usb.c
5
The main file implementing the application

## Slide 13: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 14: Example application behavior
XMC4500 General Purpose board is initialized as a USB host and provides VBUS on the USB port
When a USB flash drive is connected, LED1 (on P3.9) is turned ON after device is successfully enumerated
Host application creates a folder with the name ABSTEP and it creates 3 files, of sizes 1 KB, 2KB and 3KB using File IO calls.
The files are read back and compared. LED blinks continuously if comparison is successful, else it stays ON continuously
When USB flash drive is disconnected, LED1 is turned off

## Slide 15: Simplified example application architecture
USB controller
USB host low level driver (XMCLib)
SCSI protocol +
host mass storage bulk only transport +
host core stack
Application software
FAT file system
Low level driver based on USB host CMSIS API
Block device API
File I/O API
FAT file system is based on a freely available implementation
USB stack and mass storage class implementation is based on a freely available stack known as LUFA

## Slide 16: Example application data flow
Application software launches a file IO request using FAT file IO API
FAT file system converts the file IO calls in to block device calls.
Blocks are read and written using the standard SCSI commands and the mass storage bulk only transport protocol state machine
Data is transferred to/from USB mass storage device using low level driver APIs
USB controller
USB host low level driver (XMCLib)
SCSI protocol +
host mass storage bulk only transport +
host core stack
Application software
FAT file system

## Slide 17: Application – overview of main.c
2
1
2
Clock setup for XMC4500
1
Select VBUS pin P3.2
3
3
Initialize USB host
5
4
6
4
Fetch descriptors and match it to mass storage device
5
Demo application function
6
Manage connection events and initiate enumeration

## Slide 18: Application – configure time delay API
The USB stack uses timing delay of the order of several tens of milliseconds to comply with the specification
Port the time delay API if required. In the example code, the SysTick timer is used.
Ensure timer is calibrated

## Slide 19: Application - callbacks
Application registers for the following event callbacks

## Slide 20: Application – Implement and register required callbacks
1
1
Implement call back function

## Slide 21: Application – Implement and register required callbacks
2
3
2
Register call back function
3
Call initialization function

## Slide 22: Application – file transfer demo
File I/O APIs are called to transfer files between host and device
Function FATFS_TestDemo() demonstrates file accesses

## Slide 23: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 24: How to test
1
Build and download project into XMC4500 General Purpose board
1
2
Start
debugger
3
Start the execution by
pressing the run button
3
2

## Slide 25: Example application behavior
Disconnect the USB flash drive and connect to a Windows laptop to confirm presence of files.

## Slide 26: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 27: Debug Hints
Check VBUS is available and within permissible range (4.4V to 5.25V) on the USB host port receptacle. Lower VBUS voltages due to excessive current draw may cause USB devices to disconnect intermittently or fail enumeration. Try connecting a different USB device.
Long cables may cause malfunction due to signal quality issues. Use short cables if possible.
Test Point

## Slide 28: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 29: Further reading
USB specifications and Micro-USB cables and connectors specification
  http://www.usb.org/developers/docs/usb20_docs/
Mass storage class specifications
    Mass storage class specification overview
    Mass storage class bulk only
  http://www.usb.org/developers/docs/devclass_docs/
SCSI specifications
  www.t10.org
CMSIS USB host API specification
  https://www.keil.com/pack/doc/CMSIS/Driver/html/group__usb__interface__gr.html

## Slide 30: Further reading
FAT file system
  http://elm-chan.org/fsw/ff/00index_e.html
LUFA USB stack
  http://www.fourwalledcubicle.com/index.php
Books
  USB Complete: The Developer's Guide, Jan Axelson
  USB Mass Storage: Designing and Programming Devices and Embedded Hosts, Jan Axelson

## Slide 31: Contents
Overview
Requirements
Setup
Implementing the application
How to test
Debug hints
Further reading
Limitations
1
2
3
4
5
6
7
8

## Slide 32: Limitations
FAT File system supports only short file names i.e. in 8.3 format.
USB Hubs are not supported
Over current protection is not supported
DMA Transfers are not supported
Low level driver does not support isochronous transfers